## Slide 1: Uncertainty in Postprandial Model Identification in type 1 Diabetes
Alejandro José Laguna Sanz
Supervisors:
Jorge Bondia Company
Paolo Rossetti

## Slide 2: Outline
The issue of variability in the treatment of type 1 diabetes: role of an Artificial Pancreas
State of the art: Predicting blood glucose
Objective I: Optimal experiment design
Objective II: CGM Statistical modeling
Objective III: New methods for characterization of variability
  Interval identification: proof of concept
  In-patient interval identification
  Out-patient interval identification
Final conclusions and future work
Notes: I will start exposing the problem of variability in diabetes
Not repeat T1DM every objective.
Objectives are results

## Slide 3: Diabetes
http://www.idf.org/diabetesatlas
State of the art
Introduction
Objective III
Objective II
Objective I
Conclusions
Notes: 10% type 1
The projection into the future is dangerous, but Diabetes nowadays is a real problem

## Slide 4: Metabolism
Insulin and glucagon are the main hormones in charge of glucose homeostasis.
In type 1 diabetic patients, the pancreas insulin secretion is partially or totally absent.
Glucagon function can also be damaged.
External replacement of insulin has been used since its discovery in 1921.
No insulin treatment to date has achieved glucose control objectives.
http://www.idf.org/diabetesatlas
State of the art
Introduction
Objective III
Objective II
Objective I
Conclusions
Notes: Pancreas is the main control agent in glucose homeostasis.
Click again for the cross over the pancreas.
Click again for highlighting the last sentence.

## Slide 5: Variability in diabetes
Inter-patient (population) variability
Intra-patient variability
Overlapping glucose profiles of 7 days of the same diabetic patient.
State of the art
Introduction
Objective III
Objective II
Objective I
Conclusions
Notes: Explain regions of glucose and safety concerns on the patient: Hypo Eu & Hyperglycemia. Over 140 mg/dl is hyperglycemia

## Slide 6: How to deal with variability
Closed loop: Emulation of physiological natural response of the pancreas
Patient
Insulin delivery
Glucose sensor
Control Algorithm
Meal
Safety constraints
Glucose
Disturbance
Actuator
State of the art
Introduction
Objective III
Objective II
Objective I
Conclusions
Notes: “Sensoring” is not a word
When speaking of the disturbances, introduce that the problem we focus here is the postprandial period.

## Slide 7: Technology
Biostator: The first closed loop device for diabetes
Current state of technology involves continuous glucose measurements and insulin infusion
Natural pancreatic control in a healthy person
No delay involved: Insulin secretion takes place in blood and directly in the portal system.
Glucose is “measured” in blood.
Insulin is delivered in blood, but in the peripheral system
Glucose is measured in blood.
Only valid for hospital environment.
Insulin is delivered subcutaneously.
Glucose is indirectly measured in the subcutaneous tissue.
Valid in home conditions.
Great delays and uncertainties involved.
State of the art
Introduction
Objective III
Objective II
Objective I
Conclusions

## Slide 8: Motivation
Selection of tools for characterizing variability in glucose profiles of type 1 diabetes
  1st Obtaining richer information from patient’s monitoring.
  2nd Characterizing the error in CGM since it may jeopardize variability identification.
  3rd Glucose model individualization including variability.
State of the art
Introduction
Objective III
Objective II
Objective I
Conclusions

## Slide 9: Models
Cambridge model3
Bergman model2
Modified Panunzi1
model
Minimal models
Average complexity models
Used for optimal experiment design
Used for characterization of patients and variability
1 Panunzi et al. (2007) Theoretical Biology and Medical Modelling,
2 Bergman et al. (1981) Journalof Clinical Investigation
3 Hovorka et al. (2002) Am J Physiol-Endoc M.
4 Kovatchev et al. (2009) J Diab Sci Technol.
UVA model4
Introduction
State of the art
Objective III
Objective II
Objective I
Conclusions
Notes: Cambridge i UVA son models aplicats a simuladors de pacients virtuals
Resposta a pq Cambridge i no UVA: Mateixa Complexitat, tots dos validats poblacionalment, tots dos aplicats a bucle tancat. Raons pràctiques.

## Slide 10: As illustration…
Minimal models (Bergman)
Average complexity models (Cambridge)
2 state equations + input systems
4 parameters + input parameters
5 state equations + input systems
12 parameters + input parameters
More physiologically accurate
Less computational cost
Bergman et al. (1981) Journal of Clinical Investigation
Hovorka et al. (2002) Am J Physiol-Endoc M.
Introduction
State of the art
Objective III
Objective II
Objective I
Conclusions

## Slide 11: Identification Experiments
Experiment | Type of model | Pros | Cons
Ståhl @ Sweden1 | Data based | Real life measurements Up to two hour prediction | Data from only one individual
Cescon @ Sweden2 | Data based | Use of CGM data | Data from only one individual 30 minutes prediction
Rollins @ USA3 | Data based | Use of multiple sensors Successful fit R=0.7 | Data from only one individual Absence of insulin disturbance
Georga @ Greece4 | Data based | 7 patients dataset | Poor predictions
Cameron @ USA5 | Data based | Experimental validation of the identifications | Poor predictions
Palerm @ USA6 | First principles | Good data fitting Physiology based models | Validation not satisfactory
Finan @ USA7 | Data based | Comparison against ZOH | No improvement over ZOH
Kirchsteiger @ Germany8 | Data based | Interval usage (uncertainty consideration) | No validation of the identifications performed
1 Ståhl & Johansson (2009) Mathematical Biosciences 217(2):107-117
2 Cescon et al. (2009) Insulin 2(4):6
5 Cameron et al. (2012) Journal of Process Control 22(8):1422-1432
4 Georga et al. (2011) Knowledge Oriented Applications in Data Mining
3 Rollins et al. (2010) Journal of Process Control 20(1):95-107
6 Palerm et al. (2006) EMBS Annual Conference
7 Finan et al. (2009) Journal of Diabetes Science and Technology 4(1):4-14
8 Kirchsteiger et al. (2011) IFAC World Congress 18:11761-11766
Only one experiment in literature was performed using first principles model
Few experiments were performed on more than 1 patient
Poor predictions, or non prediction at all were reported
Introduction
State of the art
Objective III
Objective II
Objective I
Conclusions
Notes: Donar entrada a la següent transparencia sobre l’assaig the kirchsteiger

## Slide 12: Interval identification
Kirchsteiger experiment was published in 2011, in the IFAC world conference in Milan.
General transfer function models were used. 1 model per day and minimizing the standard deviation of the identified parameters.
This method yields intervals parameters.
Data are not guaranteed to be enclosed.
Validation of the results is not performed with the identified interval parameters.
No validation statistics are reported.
Introduction
State of the art
Objective III
Objective II
Objective I
Conclusions

## Slide 13: Interval models
Solution is a band of possible glucose values.
Guaranteed envelope of traditional simulations.
Efficient computation.
Literature available interval models of type 1 diabetic patients:
Calm et al. published an interval approach of the Cambridge model using modal interval analysis1.
De Pereda et al. also published a Cambridge model interval solution2 using monotonicity analysis.
1 Calm et al. (2010) Journal of Clinical Investigation
2 Hovorka et al. (2002) Am J Physiol-Endoc M.
Introduction
State of the art
Objective III
Objective II
Objective I
Conclusions
Notes: Només mencionar les equacions

## Slide 14: Optimal experiment design
The objective is to design a clinical protocol for optimal patient identification.
Identifiability of two endogenous models was optimized.
  Modified Panunzi model.
  Bergman model.
Initial parameter set was reduced by means of an identifiability analysis.
D-optimality of the FIM was chosen as identifiability optimum.
Optimization was performed using SSM1 for Matlab.
1 M. Rodriguez-Fernandez et al. (2006) BMC bioinformatics, 7(1):483
Insulin
Glucose
Bolus delay
bolus
Meal
 | Upper bound | Lower Bound
Meal (gr) | 100 | 0
Bolus (IU) | 10 | 0
τ (minutes) | 300 | -60
Glucose | 250 | 70
Introduction
Objective I
Objective III
Objective II
Conclusions
State of the art
Notes: Note that more parameters does not necessarily mean better identifiability

## Slide 15: Optimal Design
Experiments are optimized by separating the input excitations.
3 days is optimal for maximizing identifiability and for practical reasons:
  1 day delayed bolus – small meal.
  2 days bolus in advance – large meal.
Every parameter’s identifiability is improved.
Qualitative results can be extracted.
Published in Laguna et al. (2010) Proceedings of the UKACC international conference
Bergman | τ (minutes) | Bolus (IU) | Meal (gr)
Day 1 | 26.43 | 10 | 85.6
Day 2 | -30.44 | 10 | 100
Day 3 | -30.71 | 10 | 100
Modified Panunzi | τ (minutes) | Bolus (IU) | Meal (gr)
Day 1 | 165.74 | 3.01 | 44.38
Day 2 | -17.83 | 10 | 100
Day 3 | -18.42 | 10 | 100
Introduction
Objective I
Objective III
Objective II
Conclusions
State of the art
Notes: Mencionar que els resultats del disseny d’experiments es va publicar al UKACC l’any 2010

## Slide 16: Protocol
Pre-prandial state | Mixed meal therapy
Glucose over 150 mg/dL or Glucose between 100 and 150 mg/dL and rising | Bolus insulin in advance 30 minutes separation 100g meal
Glucose below 100 mg/dL or Glucose between 100 and 150 mg/dL and decreasing | Delayed insulin bolus 120 minutes separation 40g meal
100 mg/dL
150 mg/dL
Meal time
Insulin bolus time
120 min
100 mg/dL
150 mg/dL
Meal time
Insulin bolus time
30 min
Published in Rossetti et al. (2012) Diabetes Technology & Therapeutics
Introduction
Objective I
Objective III
Objective II
Conclusions
State of the art
Notes: Amb aquest protocol minimitzem el risc per al pacient diabetic

## Slide 17: Dataset
Two weeks of home monitoring of 12 patients was performed using the designed protocol.
Only CGM measurements were registered, along with patient’s diary of diet and events.
The data obtained were used in a proof of concept experiment of an open loop control in the Hospital Clínic Universitari de València. The treatment delivered was calculated from models obtained from the monitoring in the previous weeks, which followed the protocol.
Feasibility of the use of models was demonstrated obtaining no worse results than an optimally adjusted therapy.
However, limitations in the models used motivated further research.
Two weeks monitored with CGM at home
Treatment calculated according to the CGM monitoring
Treatment validation in hospital
In-hospital monitoring days did not follow the protocol, but blood glucose, CGM signal and plasma insulin were registered.
12 patients, with four postprandial periods each were monitored.
Introduction
Objective I
Objective III
Objective II
Conclusions
State of the art
Published in Rossetti et al. (2012) Diabetes Technology & Therapeutics

## Slide 18: CGM error model
Two different commercial devices were used simultaneously:
  Medtronic Paradigm VEO
  Dexcom SEVEN PLUS
The error of these monitors is usually large (average of 20%) and involves delays, biases and time-correlations
Introduction
Objective II
Objective III
Conclusions
State of the art
Objective I

## Slide 19: CGM error model
Published in Laguna et al. (2013a) Biomedical Signal Processing & Control
Introduction
Objective II
Objective III
Conclusions
State of the art
Objective I
Time delay
Stationarity
Mean error related to the YSI signal gradient
Distribution
AR model fitting of the signal
Time-Correlation
Leptokurtic statistical distribution fitting
Delay calculated out of the maximum cross-correlation between the YSI and the CGM
Error standard deviation related to the YSI signal
Four distributions: Normal, Log-normal, Weibull, Logistic
Stationary signal in mean and standard deviation
Shifted signal without delay
Notes: Els resultats de tot el modelat dels CGM han estat publicats al Biomedical Signals processing & control

## Slide 20: Delay analysis
SEVEN PLUS
VEO
Introduction
Objective II
Objective III
Conclusions
State of the art
Objective I

## Slide 21: Stationarity
Pseudo-stationarity of the signal was achieved.
Mean and Standard deviation were modeled and transformed from the blood glucose signal.
The transformation is invertible for simulation purposes.
Introduction
Objective II
Objective III
Conclusions
State of the art
Objective I

## Slide 22: CGM distribution
Probability distributions and AR models were adjusted to the transformed signal.
Experimental MARD and simulated MARD were very similar (18.72% vs 17.28%) for the SEVEN PLUS monitor.
VEO monitor simulated MARD was somewhat larger than the observed (18.38% vs 14.98%).
Introduction
Objective II
Objective III
Conclusions
State of the art
Objective I

## Slide 23: CGM model
A model was developed for each CGM device analyzed.
The same structure was used for both models.
Introduction
Objective II
Objective III
Conclusions
State of the art
Objective I
being a white noise
AR model
Non-stationarity
Delay

## Slide 24: Interval Identification
classic
interval
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II

## Slide 25: Interval – Classic identification spectrum
Identification procedure:
  All calculations were performed in Matlab R2012a.
  Multi-objective optimization was performed using the εv-MOGA1 optimization algorithm.
1 Herrero et al. (2007) Computational and Ambient Intelligence
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II
Notes: Relacionar la decisió amb el CGM i els errors de modelat

## Slide 26: Pareto Front
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II
Multiple objectives:
  Je= Quadratic error to the interval
  Jw= Interval width
Notes: La identificació clàsica te error màxim perque es impossible que la curva pase per tots els punts.

## Slide 27: Complexity
Less complex
More complex
Virtual data identification
Using YSI (I)
Using CGM model (II)
Experimental identification
Using YSI
Using CGM (V)
Plasma Insulin as input (III)
Including SC Insulin model (IV)
Conclusions
Part II
Part I
Preface
Part III: Interval Identification
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II
Notes: Explicar els nombres com a referencies futures

## Slide 28: I - Virtual YSI Identification
Postprandial width | 
Mean | 62,59 (±20,85)
Max | 95,64 (±32,92)
Proof of concept.
100% of samples predicted.
14 virtual patients were generated, simulating 3 postprandial periods each
10% uncertainty introduced in insulin sensitivity and insulin elimination.
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II
Published in Laguna et al. (2012) In BMS symposium
Notes: Proba de concepte de la metodologia
Aqueste proves foren publicades al symposium BMS al 2012

## Slide 29: II - CGM Pareto front
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II

## Slide 30: II - Virtual CGM Identification
Avg2 uses the average width of the superposition of two identical days. Best correlation to variability R=0.83.
Avg3 uses the average width of the superposition of the three monitoring days. Best correlation to variability R=0.8.
Both estimators use linear regression to estimate the envelope width.
Nearest Pareto individual is chosen as the solution.
Published in Laguna et al. (2013b) Biomedical Signal Processing & Control
Validation values | Width [mg/dL] | MARD [%]
Avg2 (median) | 83.3 | 3.3
Avg3 (median) | 61.4 | 4.6
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II
Notes: Aquestes proves foren publicades al journal Biomedical signal processing & control al 2013

## Slide 31: III - Optimization index
Optimization with a compound objective yields a single individual of the Pareto front.
Cross-validation of the identifications is performed using a leave-1-day-out strategy.
Plasma insulin was initially considered an input to the system, ignoring the subcutaneous insulin model identification.
Optimization was performed using CMAES1 global search engine.
1 Hansen et al. (2004) Parallel Problem Solving from Nature-PPSN VIII
Postprandial data from 12 T1DM patients was used. Four postprandial periods of five hours were available from each patient.
Plasma insulin, plasma glucose and CGM signal were recorded frequently.
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II
Notes: Introduir la correlació creuada

## Slide 32: III - YSI Identification
Patient 2
Published in Laguna et al. (2013) Journal of Process Control
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II

## Slide 33: III - YSI Identification
Patient 11
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II

## Slide 34: III - YSI Identification
 | Width [mg/dL] | Prediction [%] | MARD [%]
Validation set | 66.4 | 52.8 | 5.56
Best case set | 94.3 | 97.3 | 0.03
Best case set is smaller (12) than the total validation set (48).
The differences displayed are statistically significant.
It is expected of larger widths to achieve better predictions.
In order to discard trivial solutions, the larger widths exhibited by the best cases have to be dedicated to simulate intra-patient variability.
If the interval fit of the identification days is not well adjusted, the identified width may be overestimated.
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II
Notes: Introduir la posibilitat de sobreestimació en l’amplaria

## Slide 35: III - Envelope Fitness
100 mg/dL
100 mg/dL
100 mg/dL
Even though width for the best case permutation were larger, envelope fitness was not, suggesting that best case is actually the largest variability displayed by the patient.
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II
Notes: Donat un lot de 3 periodes postprandials
Destacar que aquest index pot ser aplicat a qualsevol set de dades que es devideix en lots.
No dir que es dificil d’explicar. Es complexe, i matematicament s’explica amb aquestes equacions

## Slide 36: III - YSI Identification
 | Width [mg/dL] | Prediction [%] | MARD [%] | Envelope Fitness [mg/dL]
Validation set | 66.4 | 52.8 | 5.56 | 14.59
Best case set | 94.3 | 97.3 | 0.03 | 15.55
Best case set is smaller (12) than the total validation set (48).
The differences displayed are statistically significant.
It is expected of larger widths to achieve better predictions.
In order to discard trivial solutions, the larger widths exhibited by the best cases have to be dedicated to simulate intra-patient variability.
If the interval fit of the identification days is not well adjusted, the identified width may be overestimated.
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II
Notes: Introduir la posibilitat de sobreestimació en l’amplaria

## Slide 37: IV - YSIScIns Identification
Patient 6
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II

## Slide 38: V - Experimental CGM Pareto front
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II
Notes: Cada punt d’aquests fronts de Pareto s’ha obtés amb una gamma distinta

## Slide 39: V - CGM Identification
Patient 6
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II

## Slide 40: Identification summary
 | III - YSI Identification | IV - YSI SCIns Identification | V - CGM Identification
Width [mg/dL] | 66.4 | 72.7 | 85.6
Prediction [%] | 52.8 | 56.8 | 62.5
MARD [%] | 5.56 | 4.3 | 5.14
Env_fit (all data) [mg/dL] | 14.59 | 15 | 19.2
Env_fit (best cases) [mg/dL] | 15.55 | 19.7 | 20
All values are population medians.
Widths increase with the problem’s complexity, for a similar level of predictability.
Independently of the problem’s complexity, interval identification is able to use a particular combination of days to accurate predict the patient’s glucose profile.
Identified widths are always representative of displayed variability.
Introduction
Objective III
Conclusions
State of the art
Objective I
Objective II
Notes: Transparencia clau de la presentació

## Slide 41: Conclusions
A statistical model of the error of two commercial CGM devices was designed.
The model is able to reproduce in simulation the basic characteristics of the error signal.
Simple home experiments were designed for maximization of the identifiability of T1DM models.
A medical protocol was extracted from the results of the experiment design, and approved by ethical committee of the Hospital Clínic de València.
A full cross validation study was performed in real patient data, for different levels of complexity in the model and the information available.
A best case permutation was found for every identification study performed.
Widths in the best case were representative of real patient variability.
Introduction
Conclusions
State of the art
Objective I
Objective II
Objective III

## Slide 42: Future Work
Test identification methodology on larger databases.
Expand multi-objective optimization to real patient identification.
Explore possibilities of variability estimation a priori on experimental data. Test the width estimators in home environment.
Validation of protocol of optimal experiment design.
Integrate interval fitness index in the optimization algorithm.
Explore robust control applications of interval predictions.
Include the interval identification methodology in an adaptive environment for future use in artificial pancreas prototypes
Introduction
Conclusions
State of the art
Objective I
Objective II
Objective III
Notes: Emprar optimització mult-objectiu significa superar les dificultats tècniques.

## Slide 43: Scientific Production
Journal papers:
  Rossetti P, Ampudia-Blasco F J, Laguna, A J, Revert A, Vehí J, Ascaso, J F, Bondia J. Evaluation of a Novel Continuous Glucose Monitoring-Based Method for Mealtime Insulin Dosing -the iBolus- in Subjects with Type 1 Diabetes Using Continuous Subcutaneous Insulin Infusion Therapy: A Randomized Controlled Trial. Diabetes Technology & Therapeutics (2012), 14(11), 1043-1052.
  Laguna A J, Rossetti P, Ampudia-Blasco F J, Vehí J, Bondia J. Postprandial performance of Dexcom® SEVEN® PLUS and Medtronic® Paradigm® Veo™: Modeling and statistical analysis, Biomedical Signal Processing & Control (2013), http://dx.doi.org/10.1016/j.bspc.2012.12.003
  Laguna A J, Rossetti P, Ampudia-Blasco F J, Vehí J, Bondia J. Identification of intra-patient variability in the postprandial response of patients with type 1 diabetes, Biomedical Signal Processing & Control (2013), http://dx.doi.org/10.1016/j.bspc.2013.07.003
  Laguna A J, Rossetti P, Ampudia-Blasco F J, Vehí J, Bondia J. Experimental blood glucose interval identification of patients with type 1 diabetes, Journal of Process Control (2013), 24(1), 171-181.
Conference papers:
  Laguna A J, Rossetti P, Ampudia-Blasco F J, Vehí J, Bondia J. (2010, September). Optimal design for individual model identification based on ambulatory continuous glucose monitoring in patients with type 1 diabetes. UKACC International Conference on Control 2010 (pp. 1-6).
  Bondia J, Laguna A J, Rossetti P, Ampudia-Blasco F J, Vehí J. (2011, August). On the Use of Hard/soft Specifications to Deal with Intra-Patient Variability in Postprandial Glucose Control in Type 1 Diabetes. 2011 IFAC World Congress (Vol. 18, No. 1, pp. 8347-8353).
  Laguna A J, Rossetti P, Ampudia-Blasco F J, Vehí J, Bondia J. (2012, August). Identification of intra-patient variability in the postprandial response of patients with type 1 diabetes. BMS symposium (50, 1-6).
8 abstracts & posters on international conferences.
Introduction
Conclusions
State of the art
Objective I
Objective II
Objective III

## Slide 44
Contact:
Alejandro José Laguna Sanz
+34 654473072
allasan@upv.es